# STILMAT PRINZ – Carpet - closed

# Text for invitation to tender

| Description: | Closed, hard-wearing entrance mat , for laying on the floor. Custom produced mats to fit width and walking depth specifications perfectly. Suitable for wheeled traffic. Any geometric shape is available on demand. |
| --- | --- |
| Model | PRINZ ( Carpet) |
| Tread surface (inlay): | High quality dust control carpet, durable and luxurious character. Made from 100% Polyamide |
| Ideal for | Fine dirt and moisture |
| Colors: | Black, Grey, Brown… |
| Version | Closed |
| Code | JCC |
| Approx. height (mm) | 12 mm |
| Entrance position | Indoors |
| Zones: I II III | Zone: III |
| Load | From Normal to Heavy |
| Footfall | Daily footfall up to 1000 |
| Roll-over and drive-over capability: | Wheelchairs, Prams, Hand and Light shopping trolleys |
| Support chassis | Made from rigid anodized aluminum with rubber sound insulation underlay |
| Aluminum material thickness (mm) | 1.2 |
| Connection | Strong and flexible PVC connection strip |
| Standard profile clearance approx. (mm) | 0 mm, closed system |
| Slip resistance | R 11 slip resistance as per DIN 51130 |
| Logo options | Logo engraving |
| Contact | STILMAT |