# STILMAT ROYAL – Lux Brush - closed

# Text for invitation to tender

| Description: | Closed hardwearing aluminum entrance mat for laying on the floor. Custom produced mats to fit width and walking depth specifications perfectly. Suitable for wheeled traffic. Any geometric shape is available on demand. |
| --- | --- |
| Model | ROYAL (Lux Brush) |
| Tread surface (inlay): | Lux brushes recessed, robust |
| Ideal for | Coarse dirt |
| Colors: | Black, Grey |
| Version | Closed system |
| Code | RCB |
| Approx. height (mm) | 19 mm |
| Entrance position | Outdoors |
| Zones: I – II - III | Zone: I |
| Load | From Normal to Heavy |
| Footfall | Daily footfall up to 1500 |
| Roll-over and drive-over capability: | Wheelchairs, Prams, Hand and Light shopping trolleys |
| Support chassis | Made from rigid anodized aluminum with rubber sound insulation underlay |
| Aluminum coating: | Fully anodized, to increase resistance to corrosion and wear. More aesthetically pleasing finish and harder surface than pure aluminum. |
| Aluminum material thickness (mm) | 1.2 |
| Connection | Strong PVC connection strip, the entire width |
| Standard profile clearance approx. (mm) | 0 mm closed system |
| Slip resistance | R 13 slip resistance as per DIN 51130 |
| Logo options | Logo engraving |
| Contact | STILMAT |