# STILMAT BARON – Lux Brush/Ribbed carpet - closed

Text for invitation to tender

| Description: | Closed hardwearing aluminum entrance mat for laying on the floor. Custom produced mats to fit width and walking depth specifications perfectly. Suitable for wheeled traffic. Any geometric shape is available on demand. |
| --- | --- |
| Model | BARON (Lux brush & Ribbed carpet) |
| Tread surface (inlay): | Lux brushes recessed, robust and High quality ribbed carpet for Public buildings (A+EFL) , durable and luxurious character. Made from 100% Polyamide with gel backing. Weather-proof |
| Ideal for: | Coarse dirt, fine dirt and moisture |
| Colors: | Black, Grey, Brown… |
| Version | Closed system |
| Code | BCBL |
| Approx. height (mm) | 30 mm |
| Entrance position | Covered outdoor areas, gateways, passages |
| Zones: I – II - III | Zone: II |
| Load | Extreme |
| Footfall | Daily footfall of 5000 and up |
| Roll-over and drive-over capability: | Wheelchairs, Prams, Hand and Light shopping trolleys |
| Support chassis | Made from rigid anodized aluminum with rubber sound insulation underlay |
| Aluminum coating: | Fully anodized, to increase resistance to corrosion and wear. More aesthetically pleasing finish and harder surface than pure aluminum. |
| Aluminum material thickness (mm) | 1.2 |
| Connection | Strong PVC connection strip, the entire width |
| Standard profile clearance approx. (mm) | 0 mm closed system |
| Slip resistance | R 11 slip resistance as per DIN 51130 |
| Logo options: | Logo engraving |
| Contact | STILMAT |